## Slide 1: Engineering Mechanics: Statics (ENGR 175) Chapter 5- Equilibrium of a Rigid Body
Summer 2017
Sam Behfarshad
Camosun College
May, 29, 2017

## Slide 2: EQUILIBRIUM OF A RIGID BODY & FREE-BODY DIAGRAMS
In-Class Activities:
Check Homework
Reading Quiz
Applications
Support Reactions
Free-Body Diagrams
Concept Quiz
Group Problem Solving
Attention Quiz
Today’s Objectives:
Students will be able to:
a) Identify support reactions, and,
b) Draw a free-body diagram.

## Slide 3: READING QUIZ
1. If a support prevents translation of a body, then the support exerts a ___________ on the body.
A) Couple moment
B) Force
C) Both A and B.
D) None of the above
2. Internal forces are _________ shown on the free body diagram of a whole body.
A) Always
B) Often
C) Rarely
D) Never
Notes: Answers:
1. B
2. D

## Slide 4: APPLICATIONS
How are the idealized model and the free body diagram used to do this?
Which diagram above is the idealized model?
The truck ramps have a weight of 400 lb each.
Each ramp is pinned to the body of the truck and held in the position by a cable. How can we determine the cable tension and support reactions?

## Slide 5: APPLICATIONS (continued)
Again, how can we make use of an idealized model and a free body diagram to answer this question?
Two smooth pipes, each having a mass of 300 kg, are supported by the tines of the loader’s fork attachment.
How can we determine all the reactive forces?

## Slide 6: CONDITIONS FOR RIGID-BODY EQUILIBRIUM (Section 5.1)
For a rigid body to be in equilibrium, the net force as well as the net moment about any arbitrary point O must be equal to zero.
 F = 0 (no translation)
and  MO = 0 (no rotation)
Forces on a rigid body
In contrast to the forces on a particle, the forces on a rigid-body are not usually concurrent and may cause rotation of the body (due to moments created by the forces).
Forces on a particle

## Slide 7: THE PROCESS OF SOLVING RIGID BODY EQUILIBRIUM PROBLEMS
Finally, we need to apply the equations of equilibrium to solve for any unknowns.
For analyzing an actual physical system, first we need to create an idealized model (above right).
Then we need to draw a free-body diagram (FBD) showing all the external (active and reactive) forces.

## Slide 8: FREE-BODY DIAGRAMS (Section 5.2)
  2. Show all the external forces and couple moments. These typically include: a) applied loads, b) support reactions, and, c) the weight of the body.
Idealized model
Free-body diagram (FBD)
  1. Draw an outlined shape. Imagine the body to be isolated or cut “free” from its constraints and draw its outlined shape.

## Slide 9: FREE-BODY DIAGRAMS (continued)
  3. Label loads and dimensions on the FBD: All known forces and couple moments should be labeled with their magnitudes and directions. For the unknown forces and couple moments, use letters like Ax, Ay, MA. Indicate any necessary dimensions.
Idealized model
Free-body diagram

## Slide 10: SUPPORT REACTIONS IN 2-D
As a general rule, if a support prevents translation of a body in a given direction, then a force is developed on the body in the opposite direction.
Similarly, if rotation is prevented, a couple moment is exerted on the body in the opposite direction.
A few example sets of diagrams s are shown above. Other support reactions are given in your textbook (Table 5-1).

## Slide 11: EXAMPLE I
Given: The operator applies a vertical force to the pedal so that the spring is stretched 1.5 in. and the force in the short link at B is
20 lb.
Draw: An idealized model and free- body diagram of the foot pedal.
The idealized model
The free-body diagram
Notes: Source : Example 5.2

## Slide 12: EXAMPLE II
Given: The unloaded platform is
suspended off the edge of the oil rig. The platform has a mass of 200 kg.
Draw: An idealized model and free-body diagram of the platform.
The idealized model of the platform is considered in two dimensions because the loading and the dimensions are all symmetrical about a vertical plane passing through its center.
Notes: Source : Example 5.4

## Slide 13: EXAMPLE II (continued)
The connection at A is treated as a pin, and the cable supports the platform at B. Note the assumed directions of the forces! The point G is the center of gravity of the platform.
The idealized model
The free-body diagram

## Slide 14: CONCEPT QUIZ
1. The beam and the cable (with a frictionless pulley at D) support an 80 kg load at C. In a FBD of only the beam, there are how many unknowns?
A) Two forces and one couple moment
B) Three forces and one couple moment
C) Three forces
D) Four forces
Notes: Answers :
1. C

## Slide 15: CONCEPT QUIZ (continued)
2. If the directions of the force and the couple moments are both reversed, what will happen to the beam?
A) The beam will lift from A. B) The beam will lift at B. C) The beam will be restrained.
D) The beam will break.
Notes: Answer
2. A

## Slide 16: GROUP PROBLEM SOLVING I
A FBD of the smooth pipe which rests against the opening at the points of contact A, B, and C.
Given:
Draw:
Notes: Source : P5-35

## Slide 17: GROUP PROBLEM SOLVING I (continued)
The idealized model
300 N
0.5m
0.5m
0.15m
0.26m
30
30
NC
NB
NA
The free body diagram

## Slide 18: GROUP PROBLEM SOLVING II
Draw a FBD of the bent rod supported by a smooth surface at B and by a collar at A, which is fixed to the rod and is free to slide over the fixed inclined rod.
Given:
Draw:
Notes: Source : P5-25

## Slide 19: GROUP PROBLEM SOLVING II (continued)
The idealized model
RA
RB
3
4
5
12
The free body diagram

## Slide 20: EQUATIONS OF EQUILIBRIUM & TWO- AND THREE-FORCE MEMEBERS
Today’s Objectives:
You will be able to:
a) Apply equations of equilibrium to solve for unknowns, and,
b) Recognize two-force members.

## Slide 21: APPLICATIONS
The uniform truck ramp has a weight of 400 lb.
The ramp is pinned at A and held in the position by the cables.
How can we determine the forces acting at the pin A and the force in the cables?
A

## Slide 22: APPLICATIONS (continued)
An 850 lb engine is supported by three chains, which are attached to the spreader bar of a hoist.
You need to check to see if the breaking strength of any of the chains is going to be exceeded. How can you determine the force acting in each of the chains?

## Slide 23: EQUATIONS OF EQUILIBRIUM (Section 5.3)
 Fx = 0  Fy = 0  MO = 0
where point O is any arbitrary point.
Please note that these equations are the ones most commonly used for solving 2-D equilibrium problems. There are two other sets of equilibrium equations that are rarely used. For your reference, they are described in the textbook.
A body is subjected to a system of forces that lie in the x-y plane. When in equilibrium, the net force and net moment acting on the body are zero (as discussed earlier in Section 5.1). This 2-D condition can be represented by the three scalar equations:

## Slide 24: TWO-FORCE MEMBERS & THREE FORCE-MEMBERS (Section 5.4)
If we apply the equations of equilibrium to such a member, we can quickly determine that the resultant forces at A and B must be equal in magnitude and act in the opposite directions along the line joining points A and B.
The solution to some equilibrium problems can be simplified if we recognize members that are subjected to forces at only two points (e.g., at points A and B in the figure below).

## Slide 25: EXAMPLES OF TWO-FORCE MEMBERS
This fact simplifies the equilibrium analysis of some rigid bodies since the directions of the resultant forces at A and B are thus known (along the line joining points A and B).
In the cases above, members AB can be considered as two-force members, provided that their weight is neglected.

## Slide 26: STEPS FOR SOLVING 2-D EQUILIBRIUM PROBLEMS
1. If not given, establish a suitable x - y coordinate system.
2. Draw a free-body diagram (FBD) of the object under analysis.
3. Apply the three equations of equilibrium (E-of-E) to solve for the unknowns.

## Slide 27: IMPORTANT NOTES
1. If there are more unknowns than the number of independent equations, then we have a statically indeterminate situation. We cannot solve these problems using just statics.
2. The order in which we apply equations may affect the simplicity of the solution. For example, if we have two unknown vertical forces and one unknown horizontal force, then solving  FX = 0 first allows us to find the horizontal unknown quickly.
3. If the answer for an unknown comes out as negative number, then the sense (direction) of the unknown force is opposite to that assumed when starting the problem.

## Slide 28: EXAMPLE
1. Put the x and y-axes in the horizontal and vertical directions, respectively.
2. Determine if there are any two-force members.
3. Draw a complete FBD of the boom.
4. Apply the E-of-E to solve for the unknowns.
Given: The 4kN load at B of the beam is supported by pins at A and C.
Find: The support reactions at A and C.
Plan:
Notes: Source : F5-2

## Slide 29: EXAMPLE (continued)
Note that the negative signs means that the reactions have the opposite directions to that assumed (as originally shown on FBD).
Note: Upon recognizing CD as a two-force member, the number of unknowns at C is reduced from two to one. Now, using E-o-f E, we get,
 + FX = AX + 11.31 cos 45 = 0; AX = – 8.00 kN
 + FY = AY + 11.31 sin 45 – 4 = 0; AY = – 4.00 kN
+ MA = FCD sin 45  1.5 – 4  3 = 0
FCD = 11.31 kN or 11.3 kN
FBD of the beam:
AX
AY
A
1.5 m
C
B
4 kN
FCD
45°
1.5 m

## Slide 30: GROUP PROBLEM SOLVING
a) Establish the x–y axis system.
b) Draw a complete FBD of the beam.
c) Apply the E-of-E to solve for the unknowns.
Given: The beam is supported by the roller at A and a pin at B.
Find: The reactions at points A and B on the beam.
Plan:
3 kN/m
Notes: Source : P5-22

## Slide 31: GROUP PROBLEM SOLVING (continued)
3 kN/m
FBD of the beam
NA
By
Bx
2 m
4 m
3 m
30
30
12 kN
First, write a moment equation about point B. Why point B?
+  MB = – (NA cos 30)  (4 + 3 cos 30) – (NA sin 30)  (3 sin 30) + 12  2 = 0
NA = 3.713 = 3.71 kN
Note that the distributed load has been reduced to a single force.

## Slide 32: GROUP PROBLEM SOLVING (continued)
3 kN/m
FBD of the beam
NA
By
Bx
2 m
4 m
3 m
30
30
12 kN
Now write the  FX =  FY = 0 equations.
 +  FX = 3.713 sin 30 – Bx = 0
 +  FY = 3.713 cos 30– 12 + By = 0
Solving these two equations, we get Bx = 1.86 kN 
By = 8.78 kN 
Recall NA = 3.713 =3.71 kN

## Slide 33: ATTENTION QUIZ
1. Which equation of equilibrium allows you to determine FB right away?
A)  FX = 0 B)  FY = 0
C)  MA = 0 D) Any one of the above.
2. A beam is supported by a pin joint and a roller. How many support reactions are there and is the structure stable for all types of loadings?
A) (3, Yes) B) (3, No)
C) (4, Yes) D) (4, No)
AX
A
B
FB
AY
100 lb
Notes: Answers:
1. C
2. B

## Slide 34: 3-D FREE-BODY DIAGRAMS, EQUILIBRIUM EQUATIONS, CONSTRAINTS AND STATICAL DETERMINACY
Today’s Objective:
You will be able to:
a) Identify support reactions in 3-D and draw a free-body diagram, and,
b) Apply the equations of equilibrium.

## Slide 35: APPLICATIONS
Ball-and-socket joints and journal bearings are often used in mechanical systems. To design the joints or bearings, the support reactions at these joints and the loads must be determined.

## Slide 36: APPLICATIONS (continued)
If A is moved to a lower position D, will the force in the rod change or remain the same? By making such a change without understanding if there is a change in forces, failure might occur.
The tie rod from point A is used to support the overhang at the entrance of a building. It is pin connected to the wall at A and to the center of the overhang B.

## Slide 37: APPLICATIONS (continued)
The floor crane, which weighs 350 lb, is supporting a oil drum.
How do you determine the largest oil drum weight that the crane can support without overturning?

## Slide 38: SUPPORT REACTIONS IN 3-D (Table 5-2)
As a general rule, if a support prevents translation of a body in a given direction, then a reaction force acting in the opposite direction is developed on the body. Similarly, if rotation is prevented, a couple moment is exerted on the body by the support.
A few examples of supports are shown above. Other support reactions are given in your textbook (Table 5-2).

## Slide 39: IMPORTANT NOTE
A single bearing or hinge can prevent rotation by providing a resistive couple moment. However, it is usually preferred to use two or more properly aligned bearings or hinges. In these cases, only force reactions are generated and no moment reactions are created.

## Slide 40: EQUATIONS OF EQUILIBRIUM (Section 5.6)
As stated earlier, when a body is in equilibrium, the net force and the net moment equal zero, i.e.,  F = 0 and  MO = 0 .
These two vector equations can be written as six scalar equations of equilibrium (E-of-E). These are
FX =  FY =  FZ = 0
MX =  MY =  MZ = 0
The moment equations can be determined about any point. Usually, choosing the point where the maximum number of unknown forces are present simplifies the solution. Any forces passing through the point where moments are taken do not appear in the moment equation.

## Slide 41: CONSTRAINTS AND STATICAL DETERMINACY (Section 5.7)
Redundant Constraints: When a body has more supports than necessary to hold it in equilibrium, it becomes statically indeterminate.
A problem that is statically indeterminate has more unknowns than equations of equilibrium.
Are statically indeterminate structures used in practice? Why or why not?

## Slide 42: IMPROPER CONSTRAINTS
In some cases, there may be as many unknown reactions as there are equations of equilibrium.
However, if the supports are not properly constrained, the body may become unstable for some loading cases.
Here, while we have 6 unknowns, there is nothing restricting rotation about the AB axis!

## Slide 43: READING QUIZ
1. If a support prevents rotation of a body about an axis, then the support exerts a ________ on the body about that axis.
  A) Couple moment B) Force
  C) Both A and B. D) None of the above.
When doing a 3-D problem analysis, you have ________ scalar equations of equilibrium.
A) 3 B) 4
  C) 5 D) 6
Notes: ANSWERS:
1. A
2. D

## Slide 44: EXAMPLE I
a) Use the established x, y and z-axes.
b) Draw a FBD of the rod.
c) Write the forces using scalar equations.
d) Apply scalar equations of equilibrium to solve for the unknown forces.
Given: The rod, supported by thrust bearing at A and cable BC, is subjected to an 80 lb force.
Find: Reactions at the thrust bearing A and cable BC.
Plan:
Notes: Source : F5-12

## Slide 45: EXAMPLE I (continued)
Applying scalar equations of equilibrium in appropriate order, we get
F X = AX = 0; AX = 0
F Z = AZ + FBC – 80 = 0;
M Y = – 80 ( 1.5 ) + FBC ( 3.0 ) = 0;
Solving the last two equations: FBC = 40 lb, AZ = 40 lb
FBD of the rod:

## Slide 46: EXAMPLE I (continued)
FBD of the rod
M X = ( MA) X + 40 (6) – 80 (6) = 0 ; (MA ) X= 240 lb ft CCW
M Z = ( MA) Z = 0 ; (MA ) Z = 0
= 40 lb
Now write scalar moment equations about what point?
Point A!

## Slide 47: EXAMPLE II
a) Use established x, y and z-axes.
b) Draw a FBD of the plate.
c) Write the forces using scalar equations.
d) Apply scalar equations of equilibrium to solve for the unknown forces.
Given: The uniform plate has a weight of 500 lb, supported by three cables.
Find: The tension in each of the supporting cables.
Plan:
Notes: Source : F5-7

## Slide 48: EXAMPLE II (continued)
FBD of the plate:
Applying scalar equations of equilibrium:
 Fz = TA + TB + TC – 200 – 500 = 0 (1)
 Mx = TA (3) + TC (3) – 500 (1.5) – 200 (3) = 0 (2)
 My = – TB (4) – TC (4) + 500 (2) + 200 (2) = 0 (3)
1.5 ft
TB
TA
TC
500 lb
200 lb

## Slide 49: EXAMPLE II (continued)
 Fz = TA + TB + TC – 200 – 500 = 0 (1)
 Mx = TA (3) + TC (3) – 500 (1.5) – 200 (3) = 0 (2)
 My = – TB (4) – TC (4) + 500 (2) + 200 (2) = 0 (3)
Using Eqs. (2) and (3), express TA and TB in terms of TC:
Eq. (2)  TA = 450 – TC
Eq. (3)  TB = 350 – TC
Substituting the results into Eq. (1) & solving for TC
Eq. (1)  (450 – TC ) + (350 – TC) + TC – 200 – 500 = 0
TC = 100 lb 
TA = 350 lb  and TA = 250 lb 

## Slide 50: GROUP PROBLEM SOLVING
a) Draw a FBD of the rod.
b) Apply scalar equations of equilibrium to solve for the unknowns.
Given: A bent rod is supported by smooth journal bearings at A, B, and C. F=800 N. Assume the rod is properly aligned.
Find: The reactions at all the supports.
Plan:
Notes: Source : P5-73

## Slide 51: GROUP PROBLEM SOLVING (continued)
The x, y and z components of force F are
Fx = (800 cos 60°) cos 30° = 346.4 N
Fy = (800 cos 60°) sin 30° = 200 N
Fz = 800 sin 60° = 692.8 N
F = 346.4 i + 200 j + 692.8 k
A FBD of the rod
F
Cx
Cy
By
Bz
Ax
Az
y
x
z
2 m
0.75 m
1 m
2 m

## Slide 52: GROUP PROBLEM SOLVING (continued)
Applying scalar equations of equilibrium, we get
 Fx = Ax + Cx + 346.4 = 0 (1)
 Fy = 200 + By + Cy = 0 (2)
 Fz = Az + Bz – 692.8 = 0 (3)
 Mx = – Cy (2) + Bz (2) – 692.8(2) = 0 (4)
 My = Bz (1) + Cx (2) = 0 (5)
 Mz = – Cy (1.75) – Cx (2) – By (1) – 346.4(2) = 0 (6)
Solving Eqs. (1) to (6),
Ax = 400 N, By = 600 N, Cx = 53.6 N
Az = 800 N, Bz = -107 N, Cy = 800 N
A FBD of the rod
F
Cx
Cy
By
Bz
Ax
Az
y
x
z
2 m
0.75 m
1 m
2 m
Recall F = 346.4 i + 200 j + 692.8 k

## Slide 53: ATTENTION QUIZ
1. A plate is supported by a ball-and-socket joint at A, a roller joint at B, and a cable at C. How many unknown support reactions are there in this problem?
A) Four forces and two moments
B) Six forces
C) Five forces
D) Four forces and one moment
Notes: ANSWER:
1. C

## Slide 54: ATTENTION QUIZ
2. What will be the easiest way to determine the force reaction BZ ?
A) Scalar equation  FZ = 0
B) Vector equation  MA = 0
C) Scalar equation  MZ = 0
D) Scalar equation  MY = 0
Notes: ANSWERS:
2. D