## Slide 1: Engineering Mechanics: Statics (ENGR 175) Chapter 9- Center of Gravity and Centroid Part 1
Summer 2017
Sam Behfarshad
Camosun College
June, 5th , 2017

## Slide 2: CENTER OF GRAVITY, CENTER OF MASS AND CENTROID OF A BODY
Today’s Objective :
Students will:
a) Understand the concepts of center of gravity, center of mass, and centroid.
b) Be able to determine the location of these points for a body.

## Slide 3: APPLICATIONS
How can we determine these resultant weights and their lines of action?
To design the structure for supporting a water tank, we will need to know the weight of the tank and water as well as the locations where the resultant forces representing these distributed loads act.

## Slide 4: APPLICATIONS (continued)
One of the important factors in determining its stability is the SUV’s center of mass.
Should it be higher or lower to make a SUV more stable?
How do you determine the location of the SUV’s center of mass?
One concern about a sport utility vehicle (SUV) is that it might tip over when taking a sharp turn.

## Slide 5: APPLICATIONS (continued)
Integration must be used to determine total weight of the goal post due to the curvature of the supporting member.
How do you determine the location of overall center of gravity?
To design the ground support structure for a goal post, it is critical to find total weight of the structure and the center of gravity’s location.

## Slide 6: CONCEPT OF CENTER OF GRAVITY (CG)
A body is composed of an infinite number of
particles, and so if the body is located within a
gravitational field, then each of these particles will have a weight dW.
From the definition of a resultant force, the sum of moments due to individual particle weight about any point is the same as the moment due to the resultant weight located at G.
Also, note that the sum of moments due to the individual particle’s weights about point G is equal to zero.
The center of gravity (CG) is a point, often shown as G, which locates the resultant weight of a system of particles or a solid body.

## Slide 7: 09_001b

## Slide 8: 09_001c

## Slide 9: 09_002

## Slide 10: 09_003

## Slide 11: CONCEPT OF CG (continued)
If dW is located at point (x, y, z), then
The location of the center of gravity, measured from the y axis, is determined by equating the moment of W about the y-axis to the sum of the moments of the weights of the particles about this same axis.
~
~
~
x W =  x dW
~
_
Similarly,
y W =  y dW
~
_
z W =  z dW
~
_
Therefore, the location of the center of gravity G with respect to the x, y, z-axes becomes

## Slide 12: CM & CENTROID OF A BODY
By replacing the W with a m in these equations, the coordinates of the center of mass can be found.
Similarly, the coordinates of the centroid of volume, area, or length can be obtained by replacing W by V, A, or L, respectively.

## Slide 13: CONCEPT OF CENTROID
The centroid coincides with the center of mass or the center of gravity only if the material of the body is homogenous (density or specific weight is constant throughout the body).
If an object has an axis of symmetry, then the centroid of object lies on that axis.
In some cases, the centroid may not be located on the object.
The centroid, C, is a point defining the geometric center of an object.

## Slide 14: STEPS TO DETERME THE CENTROID OF AN AREA
1. Choose an appropriate differential element dA at a general point (x,y). Hint: Generally, if y is easily expressed in terms of x (e.g., y = x2 + 1), use a vertical rectangular element. If the converse is true, then use a horizontal rectangular element.
2. Express dA in terms of the differentiating element dx (or dy).
Note: Similar steps are used for determining the CG or CM. These steps will become clearer by doing a few examples.
4. Express all the variables and integral limits in the formula using either x or y depending on whether the differential element is in terms of dx or dy, respectively, and integrate.
3. Determine coordinates (x, y) of the centroid of the rectangular element in terms of the general point (x, y).
~
~

## Slide 15: READING QUIZ
1. The _________ is the point defining the geometric center of an object.
  A) Center of gravity B) Center of mass
  C) Centroid D) None of the above
2. To study problems concerned with the motion of matter under the influence of forces, i.e., dynamics, it is necessary to locate a point called ________.
A) Center of gravity B) Center of mass
C) Centroid D) None of the above
Notes: Answers:
1. C
2. B

## Slide 16: EXAMPLE I
2. dA = y dx = x3 dx
3. x = x and y = y / 2 = x3 / 2
~
~
Solution:
1. Since y is given in terms of x, choose dA as a vertical rectangular strip.
Given: The area as shown.
Find: The centroid location (x , y)
Plan: Follow the steps.
Notes: Source : F9-2

## Slide 17: EXAMPLE I (continued)
4. x = ( A x dA ) / ( A dA )
~
0 x (x3 ) d x 1/5 [ x5 ]1
0 (x3 ) d x 1/4 [ x4 ]1
= ( 1/5) / ( 1/4) = 0.8 m
1
=
=
1
0
0
y =
1
A y dA 0  (x3 / 2) ( x3 ) dx 1/14[x7]1
A dA 0  x3 dx 1/4[x4]1
1
=
~
=
= (1/14) / (1/4) = 0.2857 m
0
0

## Slide 18: EXAMPLE II
2. x = x + (1x) / 2 = (1 + x) /2 = (1 + y2)/2
3. y = y
~
~
Given: The shape and associated horizontal rectangular strip shown.
Find: dA and (x , y)
Plan: Follow the steps.
Solution:
1. dA = (1-x)dy = (1-y2)dy
x
~
y
~
~
~
Notes: Source : Preliminary Prob 9-1

## Slide 19: CONCEPT QUIZ
1. The steel plate, with known weight and non-uniform thickness and density, is supported as shown. Of the three parameters CG, CM, and centroid, which one is needed for determining the support reactions? Are all three parameters located at the same point?
A) (center of gravity, yes) B) (center of gravity, no) C) (centroid, yes) D) (centroid, no)
2. When determining the centroid of the area above, which type of differential area element requires the least computational work?
A) Vertical B) Horizontal
C) Polar D) Any one of the above.
Notes: Answers:
1. B
2. A

## Slide 20: GROUP PROBLEM SOLVING
Given: The steel plate is 0.3 m thick and has a density of 7850 kg/m3.
Find: The location of its center of mass. Also compute the reactions at A and B.
Plan:
Follow the solution steps to find the CM by integration. Then use 2-dimensional equations of equilibrium to solve for the external reactions.
Notes: Source : P9-34

## Slide 21: GROUP PROBLEM SOLVING (continued)
Solution:
1. Choose dA as a vertical rectangular strip.
3. = x
= ( y1 + y2) / 2
= ( – x) /2
2. dA = (y2 – y1) dx
  = ( + x) dx

## Slide 22: GROUP PROBLEM SOLVING (continued)
= 1.26 m and = 0.143 m
= = =
= = =
4.

## Slide 23: GROUP PROBLEM SOLVING (continued)
Place the weight of the plate at the centroid G.
Area, A = 4.667 m2
Weight, W = (7850) (9.81) (4.667) 0.3 = 107.8 kN
Here is FBD to find the reactions at A and B.
Applying Equations of Equilibrium:
+  MA = NB (2) – 107.8 (1.26) = 0
NB = 47.92 = 47.9 kN
+   FX = – Ax + 47.92 Cos 45 = 0
AX = 33.9 kN
+   FY = Ay + 47.92 Sin 45 – 107.8 = 0
AY = 73.9 kN

## Slide 24: ATTENTION QUIZ
1. If a vertical rectangular strip is chosen as the differential element, then all the variables, including the integral limit, should be in terms of _____ .
A) x B) y
C) z D) Any of the above.
2. If a vertical rectangular strip is chosen, then what are the values of x and y?
A) (x , y) B) (x / 2 , y / 2)
C) (x , 0) D) (x , y / 2)
~
~
Notes: Answers:
1. A
2. D

## Slide 25
Questions

## Slide 26
                Thank you.