## Slide 1: Engineering Mechanics: Statics (ENGR 175) Chapter 9- Center of Gravity and Centroid Part 2
Summer 2017
Sam Behfarshad
Camosun College
June, 5th , 2017

## Slide 2: COMPOSITE BODIES
Today’s Objective:
Students will be able to determine:
The location of the center of gravity (CG),
The location of the center of mass,
And, the location of the centroid using the method of composite bodies.

## Slide 3: APPLICATIONS
How can we easily determine the location of the centroid for different beam shapes?
The I-beam (top) or T-beam (bottom) shown are commonly used in building various types of structures.
When doing a stress or deflection analysis for a beam, the location of its centroid is very important.

## Slide 4: APPLICATIONS (continued)
In order to design the ground support structures, the reactions at blocks A and B have to be found. To do this easily, it is important to determine the location of the compressor’s center of gravity (CG).
If we know the weight and CG of individual components, we need a simple way to determine the location of the CG of the assembled unit.
The compressor is assembled with many individual components.

## Slide 5: CG/CM OF A COMPOSITE BODY
By replacing the W with a M in these equations, the coordinates of the center of mass can be found.
Summing the moments about the y-axis, we get
x WR = x1W1 + x2W2 + ……….. + xnWn
where x1 represents x coordinate of W1, etc..
~
~
~
~
Consider a composite body which consists of a series of particles (or bodies) as shown in the figure. The net or resultant weight is given as WR = W.
Similarly, we can sum moments about the x- and z-axes to find the coordinates of the CG.

## Slide 6: CONCEPT OF A COMPOSITE BODY
Knowing the location of the centroid, C, or center of gravity, CG, of the simple-shaped parts, we can easily determine the location of the C or CG for the more complex composite body.
Many industrial objects can be considered as composite bodies made up of a series of connected “simple-shaped” parts, like a rectangle, triangle, and semicircle, or holes.

## Slide 7: CONCEPT OF A COMPOSITE BODY (continued)
This can be done by considering each part as a “particle” and following the procedure as described in Section 9.1.
This is a simple, effective, and practical method of determining the location of the centroid or center of gravity of a complex part, structure or machine.

## Slide 8: STEPS FOR ANALYSIS
1. Divide the body into pieces that are known shapes. Holes are considered as pieces with negative weight or size.
2. Make a table with the first column for segment number, the second column for weight, mass, or size (depending on the problem), the next set of columns for the moment arms, and, finally, several columns for recording results of simple intermediate calculations.
3. Fix the coordinate axes, determine the coordinates of the center of gravity of centroid of each piece, and then fill in the table.
4. Sum the columns to get x, y, and z. Use formulas like
x = (  xi Ai ) / (  Ai ) or x = (  xi Wi ) / (  Wi )
This approach will become straightforward after doing examples!



## Slide 9: READING QUIZ
1. A composite body in this section refers to a body made of ____.
  A) Carbon fibers and an epoxy matrix in a car fender
  B) Steel and concrete forming a structure
  C) A collection of “simple” shaped parts or holes
  D) A collection of “complex” shaped parts or holes
2. The composite method for determining the location of the center of gravity of a composite body requires _______.
  A) Simple arithmetic B) Integration
  C) Differentiation D) All of the above.
Notes: Answers:
1. C
2. A

## Slide 10: EXAMPLE
Solution:
1. In this problem, the blocks A, B and C can be considered as three pieces (or segments).
Given: Three blocks are assembled as shown.
Find: The center of volume of this assembly.
Plan: Follow the steps for analysis.
A
B
C
Notes: Source : F9-12

## Slide 11: EXAMPLE (continued)
Volumes of each shape:
VA = (0.5) (1.5) (1.8) (0.5) = 0.675 m3
VB = (2.5) (1.8) (0.5) = 2.25 m3
VC = (0.5) (1.5) (1.8) (0.5) = 0.675 m3
A
B
C
 3.6 1.406 5.007 2.835
0.405
2.025
0.405
0.1688
2.813
2.025
0.675
0.5625
0.1688
0.6
0.9
0.6
0.25
1.25
3.0
1.0
0.25
0.25
0.675
2.25
0.675
A
B
C
zV (m4)
yV (m4)
xV (m4)
z (m)
y (m)
x (m)
V (m3)
Segment







## Slide 12: EXAMPLE (continued)
~
x = ( x V) / ( V ) = 1.406 / 3.6 = 0.391 m
y = ( y V) / ( V ) = 5.007 / 3.6 = 1.39 m
z = ( z V) / ( V ) = 2.835 / 3.6 = 0.788 m
~
~
V (m3) x V y V z V
(m4) (m4) (m4)
3.6 1.406 5.007 2.835



Table Summary
Substituting into the Center of Volume equations:
A
B
C

## Slide 13: CONCEPT QUIZ
1. Based on typical available centroid information, what are the minimum number of pieces to consider for determining the centroid of the area shown at the right?
A) 4 B) 3 C) 2 D) 1
2. A storage box is tilted up to clean the rug underneath the box. It is tilted up by pulling the handle C, with edge A remaining on the ground. What is the maximum angle of tilt possible (measured between bottom AB and the ground) before the box tips over?
A) 30° B) 45 ° C) 60 ° D) 90 °
3cm
1 cm
1 cm
3cm
30º
G
C
A
B
Notes: Answers:
1. B
2. C

## Slide 14: GROUP PROBLEM SOLVING
Solution:
1. This body can be divided into the following pieces: triangle (a) + rectangle (b) + quarter circular (c) – semicircular area (d). Note that a negative sign should be used for the hole!
Given: The part shown.
Find: The centroid of the part.
Plan: Follow the steps for analysis.
a
b
c
d
Notes: Source : P9-64

## Slide 15: GROUP PROBLEM SOLVING (continued)
a
b
c
d
y
Steps 2 & 3: Create and complete the table using parts a, b, c, and d. Note the location of the axis system.
26.33
– 22.5
19.00

4.5
13.5
9
– 0.67
– 18
– 13.5
9
0
1
1.5
4(3) / (3 )
4(1) / (3 )
– 4
– 1.5
4(3) / (3 )
0
4.5
9.0
9  / 4
–  / 2
Triangle a
Rectangle b
Qtr. Circle c
Semi-Circle d
y A ( in3)
x A ( in3)
y (in)
x (in)
Area A (in2)
Segment





## Slide 16: GROUP PROBLEM SOLVING (continued)
4. Now use the table data results and the formulas to find the coordinates of the centroid.
x = (  x A) / ( A ) = – 22.5 in3/ 19.0 in2 = – 1.18 in
y = (  y A) / ( A ) = 26.33 in3 / 19.0 in2 = 1.39 in


Area A x A y A
19.00 – 22.5 26.33


C
y

## Slide 17: ATTENTION QUIZ
2. For determining the centroid of the area, two square segments are considered; square ABCD and square DEFG. What are the coordinates (x, y ) of the centroid of square DEFG?
A) (1, 1) m B) (1.25, 1.25) m
C) (0.5, 0.5 ) m D) (1.5, 1.5) m
~
~
1. A rectangular area has semicircular and triangular cuts as shown. For determining the centroid, what is the minimum number of pieces that you can use?
A) Two B) Three
C) Four D) Five
2cm
2cm
2cm
4cm
x
y
A
1m
1m
y
E
F
G
C
B
x
1m
1m
D
Notes: Answers:
1. B
2. D

## Slide 18
Assignment for Chapter 9 (Ed. 14):
9.3, 9.40, 9.52, 9.73
Due June, 12th by 4:00pm
Supplementary questions for Chapter 9:
9.25, 9.29, 9.31, 9.47, 9.67, 9.69, 9.70, 9.76

## Slide 20
SGTQ
Student Generated Test Question

## Slide 21
Questions

## Slide 22
                Thank you.