## Slide 1: Engineering Mechanics: Statics (ENGR 175) Chapter 10- Moments of Inertia Part 1
Summer 2017
Sam Behfarshad
Camosun College
June, 12th , 2017

## Slide 2: DEFINITION OF MOMENTS OF INERTIA FOR AREAS, RADIUS OF GYRATION OF AN AREA
Today’s Objectives:
You will be able to:
a) Define the moments of inertia (MoI) for an area.
b) Determine the MoI for an area by integration.

## Slide 3: APPLICATIONS
Why do they usually not have solid rectangular, square, or circular cross sectional areas?
What primary property of these members influences design decisions?
Many structural members like beams and columns have cross sectional shapes like an I, H, C, etc..

## Slide 4: APPLICATIONS (continued)
This section of the book covers some parameters of the cross sectional area that influence the designer’s selection.
Do you know how to determine the value of these parameters for a given cross-sectional area?
Many structural members are made of tubes rather than solid squares or rounds.
Why?

## Slide 5: DEFINITION OF MOMENTS OF INERTIA FOR AREAS (Section 10.1)
The force on the area dA at that point is dF = p dA. The moment about the x-axis due to this force is y (dF). The total moment is A y dF = A  y2 dA =  A( y2 dA).
This sort of integral term also appears in solid mechanics when determining stresses and deflection. This integral term is referred to as the moment of inertia of the area of the plate about an axis.
Consider a plate submerged in a liquid. The pressure of a liquid at a distance y below the surface is given by p =  y, where  is the specific weight of the liquid.

## Slide 6: DEFINITION OF MOMENTS OF INERTIA FOR AREAS
For the given vertical loading P on the beam shown on the right, which shape will develop less internal stress and deflection? Why?
The answer depends on the MoI of the beam about the x-axis. It turns out that Section A has the highest MoI because most of the area is farthest from the x axis. Hence, it has the least stress and deflection.
1cm
Consider three different possible cross-sectional shapes and areas for the beam RS. All have the same total area and, assuming they are made of same material, they will have the same mass per unit length.
10cm
10cm
1cm
x
3cm
10cm
3cm
R
S
P
(C)
(B)
(A)

## Slide 7: DEFINITION OF MOMENTS OF INERTIA FOR AREAS
The moments of inertia for the entire area are obtained by integration.
Ix = A y2 dA ; Iy = A x2 dA
JO = A r2 dA = A ( x2 + y2 ) dA = Ix + Iy
The MoI is also referred to as the second moment of an area and has units of length to the fourth power (m4 or in4).
For the differential area dA, shown in the figure: d Ix = y2 dA , d Iy = x2 dA , and, d JO = r2 dA , where JO is the polar moment of inertia about the pole O or z axis.

## Slide 8: MoI FOR AN AREA BY INTEGRATION
  a) The element parallel to the axis about which the MoI is to be determined usually results in an easier solution. For example, we typically choose a horizontal strip for determining Ix and a vertical strip for determining Iy.
The step-by-step procedure is:
1. Choose the element dA: There are two choices: a vertical strip or a horizontal strip. Some considerations about this choice are:
For simplicity, the area element used has a differential size in only one direction (dx or dy). This results in a single integration and is usually simpler than doing a double integration with two differentials, i.e., dx·dy.

## Slide 9: MoI FOR AN AREA BY INTEGRATION (continued)
2. Integrate to find the MoI. For example, given the element shown in the figure above:
Iy =  x2 dA =  x2 y dx and
Ix =  d Ix =  (1 / 3) y3 dx (using the parallel axis theorem as per Example 10.2 of the textbook).
Since the differential element is dx, y needs to be expressed in terms of x and the integral limit must also be in terms of x. As you can see, choosing the element and integrating can be challenging. It may require a trial and error approach, plus experience.
b) If y is easily expressed in terms of x (e.g., y = x2 + 1), then choosing a vertical strip with a differential element dx wide may be advantageous.

## Slide 10: READING QUIZ
1. The definition of the Moment of Inertia for an area involves an integral of the form
A)  x dA. B)  x2 dA.
C)  x2 dm. D)  m dA.
2. Select the correct SI units for the Moment of Inertia for an area.
A) m3
B) m4
C) kg·m2
D) kg·m3
Notes: Answers:
1. B
2. B

## Slide 11: EXAMPLE
Solution:
Ix =  y2 dA
dA = (1 – x) dy = (1 – y3/2) dy
Ix = 0 y2 (1 – y3/2) dy
= [ (1/3) y3 – (2/9) y9/2 ] 0 = 0.111 m4
1
1
Given: The shaded area shown in the figure.
Find: The MoI of the area about the x- and y-axes.
Plan: Follow the steps given earlier.
 (x,y)
Notes: Source : F10-1, F10-3

## Slide 12: EXAMPLE (continued)
Iy =  x2 dA =  x2 y dx
=  x2 (x2/3) dx
= 0  x8/3 dx
= [ (3/11) x11/3 ]0
= 0.273 m 4
1
1
 (x,y)
In the above example, Ix can be also determined using a vertical strip.
Then Ix =  (1/3) y3 dx = 0 (1/3) x2 dx = 1/9 = 0.111 m 4
1

## Slide 13: GROUP PROBLEM SOLVING
Given: The shaded area shown.
Find: Ix and Iy of the area.
Plan:
Follow the procedure described earlier.
dx
y
(x,y)

Notes: Source : P10-17, P10-18

## Slide 14: GROUP PROBLEM SOLVING (continued)
dx
y
(x,y)

Solution:
The moment of inertia of the rectangular differential element about the x-axis is dIx = (1/3) y3 dx (see Case 2 in Example 10.2 in the textbook).

## Slide 15: GROUP PROBLEM SOLVING (continued)
where
The moment of inertia about the y-axis
dx
y
(x,y)


## Slide 16: PARALLEL-AXIS THEOREM, RADIUS OF GYRATION & MOMENT OF INERTIA FOR COMPOSITE AREAS
Today’s Objectives:
You will be able to:
Apply the parallel-axis theorem.
Determine the moment of inertia (MoI) for a composite area.

## Slide 17: APPLICATIONS
It is helpful and efficient if you can do a simpler method for determining the MoI of such cross-sectional areas as compared to the integration method.
Do you have any ideas about how this problem might be approached?
Cross-sectional areas of structural members are usually made of simple shapes or combination of simple shapes. To design these types of members, we need to find the moment of inertia (MoI).

## Slide 18: APPLICATIONS (continued)
Design calculations typically require use of the MoI for these cross-sectional areas.
This is another example of a structural member with a composite cross-area. Such assemblies are often referred to as a “built-up” beam or member.

## Slide 19: PARALLEL-AXIS THEOREM FOR AN AREA (Section 10.2)
Consider an area with centroid C. The x' and y' axes pass through C. The MoI about the x-axis, which is parallel to, and distance dy from the x ' axis, is found by using the parallel-axis theorem.
This theorem relates the moment of inertia (MoI) of an area about an axis passing through the area’s centroid to the MoI of the area about a corresponding parallel axis. This theorem has many practical applications, especially when working with composite areas.

## Slide 20: PARALLEL-AXIS THEOREM (continued)
Using the definition of the centroid:
y' = (A y' dA) / (A dA) . Now
since C is at the origin of the x' – y' axes,
y' = 0 , and hence A y' dA = 0 .
Thus IX = IX' + A dy2
Similarly, IY = IY' + A dX2 and
JO = JC + A d2
IX = A y2 dA = A (y' + dy)2 dA
= A y' 2 dA + 2 dy A y' dA + dy2 A dA
IX' is MoI about the centroid of the body.

## Slide 21: RADIUS OF GYRATION OF AN AREA (Section 10.3)
The radius of gyration has units of length and gives an indication of the spread of the area from the axes. This characteristic is important when designing columns.
Then, Ix = kxA or kx =  ( Ix / A). This kx is called the radius of gyration of the area about the x axis.
2
For a given area A and its MoI, Ix , imagine that the entire area is located at distance kx from the x axis.
A
kx
x
y
A
ky
x
y
Similarly;
ky =  ( Iy / A ) and kO =  ( JO / A )

## Slide 22: MOMENT OF INERTIA FOR A COMPOSITE AREA (Section 10.4)
The MoI about their centroidal axes of these “simpler” shaped areas are found in most engineering handbooks, with a sampling inside the back cover of the textbook.
Using these data and the parallel-axis theorem, the MoI for a composite area can easily be calculated.
A composite area is made by adding or subtracting a series of “simple” shaped areas like rectangles, triangles, and circles.
For example, the area on the left can be made from a rectangle plus a triangle, minus the interior rectangle.

## Slide 23: STEPS FOR ANALYSIS
1. Divide the given area into its simpler shaped parts.
4. The MoI of the entire area about the reference axis is determined by performing an algebraic summation of the individual MoIs obtained in Step 3. (Please note that the MoI of the hole is subtracted).
3. Determine the MoI of each “simpler” shaped part about the desired reference axis using the parallel-axis theorem ( IX = IX’ + A ( dy )2 ) .
2. Locate the centroid of each part and indicate the perpendicular distance from each centroid to the desired reference axis.
=

## Slide 24: READING QUIZ
1. The parallel-axis theorem for an area is applied between
  A) An axis passing through its centroid and any corresponding parallel axis.
  B) Any two parallel axis.
  C) Two horizontal axes only.
  D) Two vertical axes only.
2. The moment of inertia of a composite area equals the ____ of the MoI of all of its parts.
  A) vector sum
  B) algebraic sum (addition or subtraction)
  C) addition
  D) product
Notes: Answers:
1. A
2. B

## Slide 25: EXAMPLE
Given: The beam’s cross-sectional area.
Find: The moment of inertia of the area about the x-axis and the radius of gyration, kx.
Plan: Follow the steps for analysis.
Solution:
1. The cross-sectional area can be divided into three rectangles ( [1], [2], [3] ) as shown.
2. The centroids of these three rectangles are in their center. The distances from these centers to the x-axis are 175 mm, 0 mm, and -175 mm, respectively.
[3] [2] [1]
Notes: Source : F10-7 (Find Ix not Iy)

## Slide 26: EXAMPLE (continued)
Using the parallel-axis theorem,
Ix[1] = Ix[3] = Ix’ + A (dy)2
= (1/12) (200) (50)3 + (200) (50) (175)2
= 3.083×108 mm4
3. From the inside back cover of the book, the MoI of a rectangle about its centroidal axis is (1/12) b h3.
Ix[2] = (1/12) (50 mm) (300 mm)3
= 1.125×108 mm4
[3]
[1]
[2]

## Slide 27: EXAMPLE (continued)
kx =  ( Ix / A)
A = 50 (300) + 200 (50) + 200 (50) = 3.5×104 mm2
kx =  (7.291×108) / (3.5×104) = 144 mm
4. Ix = Ix1 + Ix2 + Ix3
Ix = 7.291×108 mm4
Summing these three MoIs:
Now, finding the radius of gyration:

## Slide 28: GROUP PROBLEM SOLVING
Given: The shaded area as shown in the figure.
Find: The moment of inertia for the area about the x-axis and the radius of gyration, kX.
Plan: Follow the steps for analysis.
(a)
(b)
(c)
1. The given area can be obtained by subtracting the circle (b) and the triangle (c) from the rectangle (a).
2. Information about the centroids of the simple shapes can be obtained from the inside back cover of the textbook. The perpendicular distances of the centroids from the x-axis are da = 150 mm, db = 150 mm, and dc = 200 mm.
Solution:
Notes: Source : P10-32

## Slide 29: GROUP PROBLEM SOLVING (continued)
(a)
(b)
(c)
IX = IXa – IXb – IXc
= 1.715×109 mm4
kX =  ( IX / A )
A = 350 (300) –  (75)2 – (1/2) 150 (300) = 8.071×104 mm2
kX =  1.715×109 / 8.071×104 = 146 mm
IXc = (1/36) (150) (300)3 + (1/2)(150) (300) (200)2
= 1.013×109 mm4
3. IXa = (1/12) (350) (300)3 + (350)(300)(150)2
= 3.15×109 mm4
IXb = (1/4)  (75)4 + (75)2 (150)2
= 4.224×108 mm4
Summing:
The radius of gyration:

## Slide 30
Questions

## Slide 31
                Thank you.