## Slide 1: Engineering Mechanics: Statics (ENGR 175) Chapter 10- Moments of Inertia Part 2
Summer 2017
Sam Behfarshad
Camosun College
June, 14th , 2017

## Slide 2: MASS MOMENT OF INERTIA
Today’s Objectives:
You will be able to :
a) Explain the concept of the Mass Moment of Inertia (MMI).
b) Determine the MMI of a composite body.

## Slide 3: APPLICATIONS
What property of the flywheel is most important for this use? How can we determine a value for this property?
Why is most of the mass of the flywheel located near the flywheel’s circumference?
The large flywheel in the picture is connected to a large metal cutter. The flywheel is used to provide a uniform motion to the cutting blade while it is cutting materials.

## Slide 4: APPLICATIONS (continued)
Which property (which we will call MMI) of the fan blade do you think effects the angular acceleration () the most?
How can we determine a value for this property? What is the relationship between M, MMI, and ?
If a torque M is applied to a fan blade initially at rest, its angular speed (rotation) begins to increase.

## Slide 5: MASS MOMENT OF INERTIA
T and  are related by the equation T = I  . In this equation, I is the mass moment of inertia (MMI) about the z axis.
The MMI of a body is a property that measures the resistance of the body to angular acceleration. This is similar to the role of mass in the equation F = m a. The MMI is often used when analyzing rotational motion (done in dynamics).
Consider a rigid body with a center of
mass at G. It is free to rotate about the z axis, which passes through G. Now, if we apply a torque T about the z axis to the body, the body begins to rotate with an angular acceleration .

## Slide 6: DEFINITION OF THE MMI
The MMI is always a positive quantity and has a unit of kg·m2 or slug·ft2.
Consider a rigid body and the arbitrary axis p shown in the figure. The MMI about the p axis is defined as I = m r2 dm, where r, the “moment arm,” is the perpendicular distance from the axis to the arbitrary element dm.

## Slide 7: RELATED CONCEPTS
Finally, the MMI can be obtained by integration or by the method for composite bodies. The latter method is easier for many practical shapes.
m
Parallel-Axis Theorem
Just as with the MoI for an area, the parallel-axis theorem can be used to find the MMI about a parallel axis z that is a distance d from the z’ axis through the body’s center of mass G. The formula is Iz = IG + (m) (d)2 (where m is the mass of the body).
The radius of gyration is similarly defined as
k = (I / m)

## Slide 8: READING QUIZ
1. The formula definition of the mass moment of inertia about an axis is ___________ .
A)  r dm B)  r2 dm
C)  m dr D)  m2 dr
2. The parallel-axis theorem can be applied to ________ .
A) Only the MoI B) Only the MMI
C) Both the MoI and MMI D) None of the above.
Note: MoI is the moment of inertia of an area and MMI is the mass moment inertia of a body
Notes: Answers :
1.B
2.C

## Slide 9: EXAMPLE
Given: The volume shown with r = 5 slug/ft3.
Find: The mass moment of inertia of this body about the y-axis.
Plan:
Find the mass moment of inertia of a disk element about the y-axis, dIy, and integrate.
Notes: Source : Example 10.11

## Slide 10: EXAMPLE (continued)
The mass moment of inertia of a disk about an axis perpendicular to its plane is I = 0.5 m r2.
Thus, for the disk element, we have
dIy = 0.5 (dm) x2
where the differential mass dm = r dV = rpx2 dy.
Solution:

## Slide 11: CONCEPT QUIZ
1. Consider a particle of mass 1 kg
located at point P, whose coordinates
are given in meters. Determine the MMI
of that particle about the z axis.
A) 9 kg·m2 B) 16 kg·m2
C) 25 kg·m2 D) 36 kg·m2
z
x
y
P (3,4,6)
Notes: Answers:
1.C
2.B

## Slide 12: GROUP PROBLEM SOLVING
Plan: Determine the MMI of the pendulum using the method for composite bodies. Then determine the radius of gyration using the MMI and mass values.
Solution:
1. Separate the pendulum into a square plate (P) and a slender rod (R).
Given: The pendulum consists of a 5 kg plate and a 3 kg slender rod.
Find: The radius of gyration of
the pendulum about an axis
perpendicular to the screen and passing through point G.
R
P
Notes: Source : P10-98

## Slide 13: GROUP PROBLEM SOLVING (continued)
R
P
y = ( y m) / ( m )
= {(1) 3 + (2.25) 5} / (3+5) = 1.781 m

3. The MMI data on plates and slender rods are given on the inside cover of the textbook. Using those data and the parallel-axis theorem,
IP = (1/12) 5 (0.52 + 12) + 5 (2.25  1.781)2 = 1.621 kg·m2
IR = (1/12) 3 (2)2 + 3 (1.781  1)2 = 2.830 kg·m2
2. The center of mass of the plate and rod are 2.25 m and 1 m from point O, respectively.

## Slide 14: GROUP PROBLEM SOLVING (continued)
R
P
4. IO = IP + IR = 1.621 + 2.830 = 4.45 kg·m2
5. Total mass (m) equals 8 kg
Radius of gyration
k = IO / m = 4.45 / 8 = 0.746 m

## Slide 15: ATTENTION QUIZ
1. A particle of mass 2 kg is located 1 m down the y-axis. What are the MMI of the particle about the x, y, and z axes, respectively?
A) (2, 0, 2) B) (0, 2, 2)
C) (0, 2, 2) D) (2, 2, 0)

1 m
x
y
z
Notes: Answers :
1.A
2.D

## Slide 16
Problems for Chapter 9 (Ed. 14):
10.10, 10.31, 10.32, 10.91, 10.105

## Slide 17
Questions

## Slide 18
                Thank you.